## Slide 1: MILP Model for Aggregate Planning
Decision variables:
  workforce level
  hired and laid-off
  production level
  inventory level
  subcontracted units
  backlogged units
  overtime hours
  These decisions have to be made for each time period

## Slide 2: MILP Model for Aggregate Planning
Objective function:
  Minimize the total cost (consists of the following costs)
    Regular-time
    Overtime
    Hiring and laying off
    Inventory holding
    Backorder
    Material
    Subcontracting
Constraints:
  Workforce level (for each time period)
  Inventory balance (for each time period)
  Production capacity (for each time period)

## Slide 3: Example
Nivia Inc. that makes several models of skateboards has to plan its production for the next 4 months. The demand information and other details are given in the below tables. One unit requires 4 hours of labor. Every month has 20 working days and the regular working hours is 8 hours per day. The overtime in a month is limited to 200 hours. Workforce level at the beginning of Month 1 is 5. Initial and ending inventory are to be zero and no backorder at the end of month 4. There is no backorder at the start of the planning horizon. Prepare the aggregate plan.
Month | 1 | 2 | 3 | 4
Forecast | 1600 | 1400 | 3000 | 2400
Head | Cost (Rs)
Regular time cost | 50/hr
Overtime cost | 75/hr
Subcontracting cost | 600/unit
Inventory holding cost | 40/unit/month
Backorder cost | 300/unit/month
Hiring cost | 6000/worker
Laying off cost | 10000/worker
Cost of materials | 200/unit

## Slide 4: Aggregate Planning Example

## Slide 5: Aggregate Planning Example
=

## Slide 6: Aggregate Planning Example
Objective:
0, 0, 5, 0; , , , integers,
all variables
Constraints:

## Slide 7: Aggregate Plan
Month | No. Hired | No. Laid off | Workforce size | Overtime | Inventory | Backorder | Subcontract | Total production | Demand
0 | 0 | 0 | 5 | 0 | 0 | 0 | 0 |  | 
1 | 35 | 0 | 40 | 0 | 0 | 0 | 0 | 1600 | 1600
2 | 16 | 0 | 56 | 0 | 840 | 0 | 0 | 2240 | 1400
3 | 1 | 0 | 57 | 0 | 120 | 0 | 0 | 2280 | 3000
4 | 0 | 0 | 57 | 0 | 0 | 0 | 0 | 2280 | 2400
Total cost | 3710400 |  |  |  |  |  |  |  | 
For details and the excel file solution, see “Aggregate planning.xlsx”, sheet 1