## Slide 1: Sales and Operations Planning (Aggregate Planning)
Sales and Operations Planning:
  An aggregate planning process
  Determines the resource capacity of a firm needed to meet its demand
  Time horizon – intermediate (eg: months)
    During this time frame, the capacity expansion (through facility expansion) is not feasible
  Managing the demand
  Managing the supply

## Slide 2: Aggregate Planning
Managing the supply
Feasible courses of action to meet the fluctuating demand during the intermediate time frame:
  Hiring and laying-off of workers
  Overtime work
  Subcontracting
  Backordering
  Increase the number of standard work hours

## Slide 3: Aggregate Planning
Managing the demand
Feasible courses of action to influence the demand
  Pricing
  Promotions

## Slide 4: Aggregate planning
Strategies to adjust capacity to meet fluctuating demand
Pure strategy
  Level: Constant production plan
  Chase: Zero inventory plan
Mixed strategy
  Combination of pure strategies, incorporating additional constraints of production process

## Slide 5: Pure Strategy
Level strategy
Chase strategy
Demand
Production
Units
Units
Time
Time
Production

## Slide 6: Push and Pull Production Systems
Push versus pull: two fundamental philosophies for movement of materials in a production system
Push system: production planning is done for all levels in advance. Once production is completed, units are pushed to the next level
Pull system: items are moved from one level to the next only when requested

## Slide 7: Push and Pull Production Systems
Push system:
  Material requirements planning (MRP) , MRP II, ERP
  Based on forecasts for end items over a specified planning horizon, the MRP planning system determines production quantities for each level of the system
Pull system:
  Just-in-time (JIT), lean production, CONWIP
  Fundamental goal is to reduce work-in-process to a bare minimum
  Items are only moved when requested by the next higher level in the production process

## Slide 8: Material Requirements Planning (MRP)
The MRP explosion calculus is a set of rules for converting a master production schedule (MPS) to a build schedule for all the components comprising the end product.
The MPS is a production plan for the end item or final product by period
MPS states which end items are to be produced, when these are needed, and in what quantities
At each stage in the process, one computes the production amounts required at each level of the production process

## Slide 9: Scheduling & Sequencing
Scheduling: Establishing the timing of the use of equipment, facilities, and human activities in an organization
Effective scheduling can yield
    Cost savings
    Increase in productivity
Sequencing: Determine the order in which jobs at a work center will be processed
  Priority rules
    Simple heuristics, used to select the order in which jobs will be processed

## Slide 10: Scheduling Hierarchies

## Slide 11
Service scheduling often presents challenges not found in manufacturing
  These are primarily related to:
    The inability to store or inventory services
    The random nature of service requests
Service scheduling may involve scheduling:
  Customers
  Workforce
Scheduling the Service

## Slide 12: Scheduling Service Operations
Scheduling customers: Demand management
  Appointment systems
    Controls customer arrivals for service
  Reservation systems
    Enable service systems to formulate a fairly accurate estimate of demand on the system for a given time period
Scheduling the workforce: Capacity management
  Cyclical Scheduling
    Employees are assigned to work shifts or time slots and have days off on a repeating basis